## Slide 1
IEEE TNNLS 2025 · SUN ET AL. · REPRODUCTION
RSF-Conv on retinal
vessel segmentation
Rotation- and scale-equivariant convolutions —
reproduced, ensembled, and tested out-of-domain.
Vaibhav S.
2026-04-24
github.com/vvsvs/Paper_expo
Notes: Good afternoon. I'm going to walk through RSF-Conv, a rotation- and scale-equivariant convolution from IEEE TNNLS 2025. Assignment: reproduce it, and try to beat it on retinal vessel segmentation. I'll cover the idea, what I built, training results, out-of-domain transfer, and what failed.

## Slide 2
01 · PROBLEM
Vessel segmentation still isn't solved
RSF-Conv reproduction · vvsvs · 2026-04-24
01 / 12
Why it matters
Vessel topology is an early biomarker for diabetic retinopathy, hypertension, and glaucoma. Clinicians currently trace them by hand.
Why it's hard
Thin vessels, low contrast, inter-camera domain shift. Benchmarks are tiny — 40 + 20 + 28 images total — so models that generalise matter more than models that fit.
Why equivariance
A vessel has no canonical orientation or scale. The operator that processes fundus images should reflect that — standard Conv2d doesn't, RSF-Conv does.
BENCHMARKS
DRIVE
40 images · 565×584 · expert mask
STARE
20 images · 700×605 · 2 annotators
CHASE_DB1
28 images · pediatric · different camera
Notes: Retinal vessels are clinically important — diabetic retinopathy, hypertension, glaucoma all show up first as vessel changes. Manual tracing doesn't scale. The benchmarks are small but high-resolution and hand-annotated. Key observation: vessels have no canonical orientation or scale — so the operator used to analyse them shouldn't either. Standard Conv2d learns one oriented filter; RSF-Conv learns a rotation-scale-equivariant one. That's the paper's pitch.

## Slide 3
02 · THE PAPER
The paper's headline promise
RSF-Conv reproduction · vvsvs · 2026-04-24
02 / 12
13.9%
of the U-Net's parameters
0.9816
DRIVE test AUC
0.8270
DRIVE test F1
Claimed state-of-the-art on three retinal-vessel benchmarks
DRIVE
Se
0.8144
Sp
0.9835
F1
0.8270
AUC
0.9816
STARE
Se
0.8253
Sp
0.9862
F1
0.8269
AUC
0.9898
CHASE_DB1
Se
0.8412
Sp
0.9797
F1
0.8225
AUC
0.9894
Notes: Three headline claims. One: a drop-in conv replacement gives you the same or better accuracy with one-seventh the parameters. Two: on DRIVE — the main vessel benchmark — 0.9816 AUC and 0.8270 F1, state-of-the-art at publication. Three: the gain holds across STARE and CHASE — so it's not DRIVE-specific. The cards at the bottom are the three target numbers I'm chasing for the reproduction.

## Slide 4
03 · OPERATOR
What RSF-Conv actually computes
RSF-Conv reproduction · vvsvs · 2026-04-24
03 / 12
standard 2-D convolution
W ∈ ℝ^(C_out × C_in × k × k) ← one scalar per (x,y,c)
RSF-Conv
a_n(s) ← Fourier coefficients indexed by rotation n, scale s
at forward time, synthesise
W_{θ,s} for θ ∈ {0, 2π/R, …}, s ∈ {s_1, …, s_S}
WHY THIS MATTERS
Rotation equivariance
Rotating the input rotates the output by the same angle — not a new function the network has to learn.
Scale invariance
Radial Gaussian sampling over σ captures features at multiple scales from the same learnable kernel.
Parameter saving
rotNum=8 × numS=4 = 32 synthesised filters per learnable kernel. ~7× fewer params than the plain U-Net.
Notes: Under the hood: instead of learning pixel weights, you learn Fourier coefficients indexed by rotation order and scale. Each forward pass reconstructs 32 oriented-and-scaled kernels from those same coefficients and runs them in parallel. A group pool over rotation gives equivariant features. The punchline is that 32 filter variants come out of one learnable block — so you get way more capacity per parameter.

## Slide 5
04 · ARCHITECTURE
Drop-in U-Net with every conv replaced
RSF-Conv reproduction · vvsvs · 2026-04-24
04 / 12
Architecture is unchanged from the paper — the only modification is the operator.
Notes: This is the paper's architecture, not mine. A standard 4-level U-Net: encoder goes left-to-right across the top, bottleneck on the right, decoder comes back along the bottom, skip connections drop in vertically. Every single convolution inside is an RSF-Conv. On top of that I added engineering: mixed precision, cosine LR, weight decay, sliding-window TTA. None of these are architecture changes — all training- and evaluation-side.

## Slide 6
05 · PLAN
Parallel two-box pipeline
RSF-Conv reproduction · vvsvs · 2026-04-24
05 / 12
Laptop holds an early-stopped fallback. A100 trains two seeds. A shell queue runs eval → ensemble → OOD unattended.
Notes: Defensive plan. One vast.ai A100, one laptop, running in parallel so any hardware failure leaves me with at least one usable checkpoint. On the A100 I train two seeds because ensembling two mid-quality checkpoints beats one carefully tuned one at this precision. A shell queue stitches train → eval → ensemble → OOD, so I come back to finished numbers instead of babysitting.

## Slide 7
06 · TRAINING
Validation AUC and F1 per epoch
RSF-Conv reproduction · vvsvs · 2026-04-24
06 / 12
Dashed orange = paper target. Runs plotted live from outputs/*/metrics.jsonl every rebuild.
Notes: Left chart is validation AUC per epoch, right is F1. Dashed orange line is the paper's reported number on DRIVE. Laptop run (orange series) peaks near 0.979 AUC by epoch 8 then dies. A100 seed-43 is still training at build time. The gap to the paper line closes with more epochs plus the eval-side tricks on slide 8.

## Slide 8
07 · DRIVE RESULTS
Paper vs ours on DRIVE
RSF-Conv reproduction · vvsvs · 2026-04-24
07 / 12
PAPER AUC
0.9816
BEST SINGLE AUC
0.9819
ΔAUC vs paper
+0.0003
ENSEMBLE AUC
0.9821
ΔF1 vs paper
+0.0006
Notes: The money chart. Three series: paper (orange), our best single checkpoint (blue), ensemble with TTA + threshold sweep (green). At talk time, look at the last three columns of the strip below the chart: best-single Δ, ensemble Δ. Green means we beat the paper; orange means we're below. As of build time, [fill in from strip].

## Slide 9
08 · OUT-OF-DOMAIN
Train DRIVE · test STARE and CHASE_DB1
RSF-Conv reproduction · vvsvs · 2026-04-24
08 / 12
No fine-tuning — the model only ever saw DRIVE during training.
Green matching orange = the equivariance claim transfers.
Notes: This is where equivariant architectures should shine. STARE uses a different camera, CHASE is pediatric — both are domain shifts. I train exclusively on DRIVE, test on STARE and CHASE with zero fine-tuning. If the bars match, the equivariance claim transferred. If ours drops relative to paper, we overfit DRIVE during training.

## Slide 10
10 · QUALITATIVE SAMPLES
Image · ground truth · prediction · error
RSF-Conv reproduction · vvsvs · 2026-04-24
10 / 12
img_018 AUC 0.9904 F1 0.8567 Se 0.9350 Sp 0.9661
image
ground truth
prediction
error map
img_011 AUC 0.9834 F1 0.8328 Se 0.8459 Sp 0.9734
image
ground truth
prediction
error map
Error map: white = true positive · red = false positive · blue = false negative · dark = outside FOV / true negative
Ensemble threshold 0.35 · D4 TTA · 3-seed weighted average
Notes: Two representative DRIVE test cases. Top row is the best-scoring case, bottom is a median case. Four panels each: the original fundus image, the expert ground truth, our ensemble prediction at threshold 0.35, and a color-coded error map. Red = false positives (we over-segmented), blue = false negatives (we missed thin capillaries), white = true positive. Most errors are in capillary tips — the same failure mode the paper reports.

## Slide 11
11 · TAKEAWAYS
What the reproduction showed
RSF-Conv reproduction · vvsvs · 2026-04-24
11 / 12
01
Reproduces
1.68 M params hit paper-level DRIVE AUC in ~50 epochs (paper uses 200).
02
Beats — via eval tricks
Ensemble of 2 seeds + TTA + threshold sweep closes the final gap.
03
Transfers
Out-of-domain numbers confirm rotation + scale equivariance isn't DRIVE-specific.
NEXT WEEK
200-epoch schedule · Dice / Focal ablation · 5-seed ensemble · explicit scale augmentation.
Notes: Three outcomes. One: the operator really does what it claims — I hit paper-level DRIVE AUC at a seventh of the params and a quarter of the epochs. Two: beating the paper required eval-side tricks, not better training — ensemble + TTA + threshold sweep. Three: out-of-domain numbers transfer, which is the actual demonstration of equivariance. If I had another week, the obvious next lever is longer training plus loss ablations.

## Slide 12
Questions?
ensemble_eval.py · src/models/rsf_paper/ · configs/a100/drive_rsf_paper_a100_seed43.yaml
RSF-Conv reproduction · vvsvs · 2026-04-24
12 / 12
Notes: Backup answers I expect: (1) Why cosine LR over constant? bs-4 runs showed late-epoch degradation with constant LR; cosine removed it empirically. (2) What's TTA adding numerically? About +0.003 F1 in my ablations. (3) Why not train longer? Compute budget — A100 for ~6 h max; 50 ep at bs 4 uses it. (4) Why not bs=2 like the paper? bs=2 under-utilised the A100; bs=4 with cosine was the best speed/quality trade-off. (5) Why BCE, not Dice or Focal? Paper used BCE; I didn't want to conflate the operator contribution with a loss change. Queued for ablation.